Reinhold Mueller-Mellin, June 2003

EPHIN/AXAF Level-One Data Specification

EPHIN/AXAF Level-One data are organized in daily files with a fixed time resolution of 65.6 seconds, hence there is a maximum of 86400/65.6 = 1318 records per file. There are three different data products:

|  | Contents | File extension |
| --- | --- | --- |
| 1 | Rates data | .SCI |
| 2 | Pulse height data (all coincidence types, nominal mode) Pulse height data (only stopping types, nominal mode) Pulse height data (all coincidence types, non-nominal mode) | .PHA .PHX .PHR |
| 3 | Housekeeping data | .HSK |

Rates data

File name:		Ayyyyddd.SCI, yyyy = year, ddd = day of year

Record format:	101 ASCII numbers, separated by space

| Index | Data item | Data type | Remarks |
| --- | --- | --- | --- |
| 0 | Year | Integer | 1999 … 2015 |
| 1 | Day of year | Integer | 1 … 366 |
| 2 | Milliseconds of day | Integer | 0 … 86,400,000 |
| 3 | Minutes since 1999 201 0:00 | Floating point F11.2 | Planned launch: 20-JUL-99 (actual launch 23-JUL-99) |
| 4 | Milliseconds since year 1 | Integer | 14 characters |
| 5 | Single rate | Integer | G0 |
| 6-11 | Single rates | Integer | A00,A01,A02,A03,A04,A05 |
| 12-17 | Single rates | Integer | B00,B01,B02,B03,B04,B05 |
| 18-21 | Single rates | Integer | C0,D0,E0,F0 |
| 22-24 | Coincidence rates | Integer | P4GM,P4GR,P4S |
| 25-27 |  |  | P8GM,P8GR,P8S |
| 28-31 |  |  | H4GM,H4GR,H4S1,H4S23 |
| 32-35 |  |  | H8GM,H8GR,H8S1,H8S23 |
| 36-39 |  |  | E150,E300,E1300,E3000 |
| 40 |  |  | INT |
| 41-43 |  |  | P25GM,P25GR,P25S |
| 44-46 |  |  | P41GM,P41GR,P41S |
| 47-50 |  |  | H25GM,H25GR,H25S1,H25S23 |
| 51-54 |  |  | H41GM,H41GR,H41S1,H41S23 |
| 55-60 |  |  | CT0,CT1,CT2,CT3,CT4,CT5 |
| 61-92 | Histogram | Integer | Bin1 … Bin32 |
| 93 | Status bits 7-0 (op,err,frame) | Integer | Nominal: 64 … 71 (cycling) |
| 94 | Status bits 15-8 (CPU status) | Integer | Nominal: 29 |
| 95 | Status bits 23-16 (FMA) | Integer | Nominal: 255 |
| 96 | Status bits 31-24 (FMB) | Integer | Nominal: 127 |
| 97 | Status bits 39-32 (FMC-G,Pwr) | Integer | Nominal: 255 |
| 98 | Dummy | Integer | 666 |
| 99 | EPHIN frame length (bytes) | Integer | 1290 |
| 100 | Spare | Integer | 0 |

GM =	Particles incident parallel to sensor axis, passing through both center segments: A0 and B0 (0( ... 21()

GR =	Particles incident parallel to sensor axis, passing through corresponding ring segments: A1 and B1 or ... or A5 and B5 (0( ... 28()

S1   = 	Particles incident at oblique angle through one center segment and one ring segment: A0 and B1 or ... or A5 and B0 (0( ... 34()

S23 =	Particles incident at oblique angle through ring segments: A1 and B2 ... or A1 and B3

(0( ... 42()

S =	Sum of S1 and S23

CT =	Control channels

Note:

- All rates are given in counts/65.6 seconds.

- All rates are raw rates, i.e. not background or deadtime corrected.

- To convert coincidence rates into intensities, divide rates by the accumulation time, the geometry factor, and the energy window (see separate tables for nuclei and electrons below).

- The geometry factor is self-adaptive: on detection of countrates > 900,000 in A00, the circular segments A01-A05 and B01-B05 are disabled, reducing the geometry factor by roughly 26. They will be enabled again when A00 falls below 600,000.

- To determine the current geometry factor, look at status information in items 95 and 96 (Failure mode A or B), or  at single rates for A or B (e.g. high count in A00 with zero count in A01).

- Apply the geometry factors to the sum of rates for a given coincidence (e.g. P4GM+P4GR+P4S, or H4GM+H4GR+H4S1+H4S23). Electrons are already summed over all incident directions.

The EPHIN status word (items 93 through 97) is implemented by hardware in the onboard EPHIN electronics and telemetered to ground. Its unrestricted use requires detailed knowledge of the EPHIN hardware.

| Item | Bit | EPHIN Status Information |
| --- | --- | --- |
|  | Position | MSB |  |  |  |  |  |  | LSB | Comment |
| 93 | 7 – 0 | Op Mode | SIO Fr | SIO Ovr | SIO Par | Frame Counter | mode, error, frame count |
|  | nomional | 0 | 1 | 0 | 0 | 0 | X | X | X |  |
| 94 | 15 – 8 | N/U | Reset | Wdog | PROM | SRAM | RAM | Dwnld | Upld | CPU status |
|  | nominal | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 |  |
| 95 | 23 – 16 | Ring | FMA | FMA5 | FMA4 | FMA3 | FMA2 | FMA1 | FMA0 | Fail. Mode Det. A |
|  | nominal | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |
| 96 | 31 – 24 | N/U | FMB | FMB5 | FMB4 | FMB3 | FMB2 | FMB1 | FMB0 | Fail. Mode Det. B |
|  | nominal | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |
| 97 | 39 – 32 | Det.G | Det.A-F | An.Pow | FMG | FMF | FME | FMD | FMC | Power and Fail. mode |
|  | nominal | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |

Op mode 00 = standby, 01 = nominal operation, 10 = calibration, 11 = not allowed

# SIO Fr, Ovr, Par = Serial Input Output framing error, overrun error, parity error

Frame counter counts 65.6 s periods, X = 0 or 1, cycles through 0 … 7.

# N/U = not used

Wdog = watchdog event

Ring = automatic switching of ring segments (1: enable, 0: disable)

| Coincidence | Geometry factor [cm2 sr] | Energy range | Energy window |
| --- | --- | --- | --- |
|  | Large | Small | [MeV/n] | [MeV/n] |
| P4 | 5.14 | 0.18 | 5.0 – 8.30 | 3.3 |
| P8 | 5.14 | 0.18 | 8.30 – 25.0 | 16.7 |
| P25 | 4.77 | 0.18 | 25.0 – 41.0 | 16.0 |
| P41 | 3.80 | 0.18 | 41.0 – 53.0 | 12.0 |
| H4 | 5.14 | 0.18 | 5.0 – 8.30 | 3.3 |
| H8 | 5.14 | 0.18 | 8.30 – 25.0 | 16.7 |
| H25 | 4.77 | 0.18 | 25.0 – 41.0 | 16.0 |
| H41 | 3.80 | 0.18 | 41.0 – 53.0 | 12.0 |
| INT | 6.85 | 0.36 | e: >8.7; p,h: >53 |  |

Note:

- For the integral counter INT no energy window is given. The geometry factor is twice the forward incident factor assuming an idealized response for forward and backward incident particles. The actual factor is somewhat lower due to absorption of backward incident particles in the spacecraft matter.

- Switching ring segments off does not change the energy window

Due to multiple scattering of electrons, it is not useful to determine the geometry factor and the energy window separately. Energy in the distribution peak and the FWHM are more appropriate. Careful Monte-Carlo simulations (courtesy E. Boehm) are used to determine the intensity factors. Divide the rates by the time and by this factor to arrive at intensities.

| Coincidence | Intensity factor [cm2 sr MeV] | Energy in peak | FWHM |
| --- | --- | --- | --- |
|  | Large | Small | [MeV] | [MeV] |
| E150 | 5.1 | 0.11 | 0.55 | 0.40 |
| E300 | 19.1 | 0.48 | 1.95 | 2.30 |
| E1300 | 20.4 | 0.62 | 4.75 | 4.50 |
| E3000 | 15.0 | 0.66 | 6.95 | 4.70 |

Note:

- The intensity factors differ grossly from previously published geometry factors and energy windows for electrons because the Monte-Carlo simulation takes into account the effects of multiple scattering in a more reliable way.

  - At low energies (channel E150), electrons incident at too large angles can still be scattered into the telescope, thereby increasing the geometry factor.

  - At all energies, electrons can be stopped in passive material or create bremsstrahlung photons which escape unnoticed, thereby increasing the energy window.

Thus, the new intensity factors are considerably larger resulting in lower intensities.

For an instrument description of EPHIN, see Mueller-Mellin et al., COSTEP – Suprathermal and Energetic Particle Analyser, Solar Physics 162: 483-504, 1995. Note that the aperture foil on EPHIN/SOHO is 0.3 mil Kapton, on EPHIN/AXAF 3 mil Kapton.