RM2    June 2013

SOHO/CEPAC Raw Data Format

There are three raw science data products for CEPAC:

- Level-0 data (e.g. SO_LZ_G030_20130606_V01.DAT1)

- Near-Real-Time data (e.g. CEPSC_120201_045117.REL)

- Real-Time data (e.g. http://costep2.nascom.nasa.gov/data/gsed/2013/06/06/1535.sc)

Level-0 and Near-Real-Time data format of the CEPAC science data super frame:

| Byte address | Bytes | Example | Description | Remark |
| --- | --- | --- | --- | --- |
| 0 - 5 | 6 | 88 aa xx xx 00 ed | header |  |
| 6 - 11 | 6 | 68 43 0a be 13 40 | lobt | for 2013 06 06 15:35 |
| 12 - 15 | 4 | be ba ca fe | sync word |  |
| 16 - 17 | 2 | 01 70 dec: 368 | LION length |  |
| 18 - 19 | 2 | 05 0a dec: 1290 | EPHIN length |  |
| 20 - 21 | 2 | 16 7c dec: 5756 | ERNE length |  |
| 22 - 243 | 222 |  | LION data | 1st part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 157 | 146 |  | LION data | 2nd part |
| 158 - 243 | 86 |  | EPHIN data | 1st part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 238 | 227 |  | EPHIN data | 2nd part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 238 | 227 |  | EPHIN data | 3rd part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 238 | 227 |  | EPHIN data | 4th part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 238 | 227 |  | EPHIN data | 5th part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 238 | 227 |  | EPHIN data | 6th part |
| Find next header | 12 | 88 aa … | header/lobt | 88 has ADRS 0 |
| 12 - 80 | 69 |  | EPHIN data | 7th part |
| 81 - 243 | 163 |  | ERNE data | 1st part |
| 0 - 5880 | 5881 |  | ERNE data with header/lobt interspersed | 24 packets |
| Total | 7808 |  |  | 32 packets |

The total number of bytes is 7808. They are transmitted to the SOHO OBDH in 32 packets with packet length 244 bytes.They contain the 7414 bytes of LION + EPHIN + ERNE data plus 32 * 12 bytes for header and local onboard time (lobt) plus 10 bytes for sync and buffer lengths.

Real-Time data format of the CEPAC science data super frame:

| Byte address | Bytes | Example | Description |
| --- | --- | --- | --- |
| 0 – 1 | 2 | 09 01 | message ID |
| 2 – 3 | 2 | 1d 04 dec: 7428 | CEPAC science data, file size - 4 |
| 4 – 7 | 4 | be 0a 43 68 | bytes in reversed order |
| 8 – 11 | 4 | be ba ca fe | sync |
| 12 – 13 | 2 | 01 70 dec: 368 | LION length |
| 14 – 15 | 2 | 05 0a dec: 1290 | EPHIN length |
| 16 – 17 | 2 | 16 7c dec: 5756 | ERNE length |
| 18 – 385 | 368 |  | LION data |
| 386 – 1675 | 1290 |  | EPHIN data |
| 1676 – 7431 | 5756 |  | ERNE data |
| Total | 7432 |  |  |

The total number of bytes per file is 7432. There is a separate file for each CEPAC science data super frame, i.e. for every minute.

Attention

When LION is switched off, the 2 byte LION length shows hex: 00 00 and the data of EPHIN and ERNE are moved forward, i.e. the first EPHIN byte is found directly after the ERNE length. This is true for both formats given above.